## Slide 1
09.09.2014
Open-ETCS WP3 : API
WP3 Workshop - Brussels
Basic Principles on Time, MMU and Balise interfaces

## Slide 2
Introduction
This presentation is a working document which aim is :
  to support the API document provided by Alstom « OETCS_API Requirements » (please see this document to have full information)
  to support technical discussion of the workshop of the 9/9/2014 in Brussels
  to ensure that everyone understands in the same way the basic principles for time, MMU and balise API data management ; (principles that are suggested by the Alstom API document and that would/could/should be adopted for the WP3 modelling tasks)
This presentation is NOT exhaustive, it is simplified :
  it only provides the BASIC principles ; the nominal CASES, the most usual cases
  It does NOT present the degraded and special cases (which nevertheless HAVE to be taken into account for the modelling tasks and for the design the OETCS application in general)

## Slide 3
ETCS TIME
0
ETCS Time is equal to 0 at power-up of the EVC
ETCS Time is always increasing as long as the EVC is powered
ETCS Time does not exist anymore when the EVC is powered-off
ETCS Time is equal to 0 at power-up of the EVC
« True »
« exact »
Time
Not known by the EVC.
See http://en.wikipedia.org/wiki/Time
ETCS time
MAX
ETCS
time
ETCS Stops working when ETCS Time reaches MAX_ETCS_Time
ETCS Time does not exist anymore when the EVC is crashed or
powered-off
POWER-ON
POWER-ON
POWER-ON
ETCS time is SIL4 and its accuracy is defined by the Unisig. (0,1%)
OETCS ASW
ETCS time
0.01s * (2exp31-1) = 248 days
(But this value can be limited by the platform)

## Slide 4
CAB
B
CAB
A
CAB
B
CAB
A
TRACK
Train Movement
Train Movement
CAB
B
CAB
A
No Movement
ETCS distance counter will ALWAYS INCREASE (SIGNED)
ETCS Speed will ALWAYS be POSITIVE (UNSIGNED)
ETCS Direction will ALWAYS be « from CAB B to CAB A » = « FORWARD »
ETCS Motion will be TRUE
ETCS distance counter will ALWAYS DECREASE (SIGNED)
ETCS Speed will ALWAYS be POSITIVE (UNSIGNED)
ETCS Direction will ALWAYS be « from CAB A to CAB B » = « REVERSE »
ETCS Motion will be TRUE
ETCS distance counter will be CONSTANT
ETCS Speed will be ZERO
ETCS Direction will be Undefined (Unkwown)
ETCS Motion will be FALSE
ETCS MMU

## Slide 5
ETCS DISTANCE
0
ETCS distance is equal to 0 at power-up of the EVC
ETCS distance (min, nom and max) is always increasing as long as the EVC is powered
ETCS distance does not exist anymore when the EVC is powered-off
ETCS distance is equal to 0 at power-up of the EVC
Time
ETCS distance
MAX
ETCS
distance
ETCS Stops working when ETCS distance reaches MAX_ETCS_distance
(e.g 15.000.000 m)
ETCS distance does not exist anymore when the EVC is crashed or
powered-off
POWER-ON
POWER-ON
Scenario : Train always runs into the same direction (from CABB to CABA)
at a constant speed (not equal to 0)
CAB
B
CAB
A
POWER-ON
nominal
max
min
ETCS nominal distance is always inside the range [min distance, max distance] (SIL4).
Assumption : Imax distance – min distanceI is NEVER DECREASING
OETCS ASW
ETCS distance
Confidence interval

## Slide 6
ETCS DISTANCE
Scenario :
Train power-up
Train goes to constant speed forward
Train STOPs
Train goes to constant speed in reverse
Train STOPs
ETCS
distance
Track
0
Real position on track
ETCS distance max
ETCS distance min
ETCS distance nom
Time
To simplify, acceleration is not taken into account in the drawing (infinite acceleration/deceleration values)
OETCS ASW
ETCS distance
CONFIDENCE INTERVAL
CONFIDENCE INTERVAL

## Slide 7
ETCS SPEED, MOTION and DIRECTION
Scenario :
Train power-up
Train goes to constant speed forward
Train STOPs
Train goes to constant speed in reverse
Train STOPs
Motion detection
Direction detection
True
False
Forward
Unknown
Reverse
Speed (m/s)
max
nominal
min
0
Time
Time
Time
max
min
nominal
To simplify, acceleration is not taken into account in the drawing.

## Slide 8
BALISE

## Slide 9
CYCLE i-1
CYCLE i
CYCLE i+1
Input
Application
Ouput
Input
Application
Ouput
Input
Application
Ouput
The application is activated once per cycle
Constants : T_CYCLE_MIN, T_CYCLE_MAX, T_INPUT_MIN, T_INPUT_MAX, T_APPLICATION_MIN, T_APPLICATION_MAX,
T_OUTPUT_MIN, T_OUTPUT_MAX (all durations)
  T_CYCLE_MIN < T_CYCLE (current cycle) < T_CYCLE_MAX
  T_INPUT_MIN < T_INPUT (current cycle) < T_INPUT_MAX
  T_APPLICATION_MIN (current cycle) < T_APPLICATION < T_APPLICATION_MAX
  T_OUTPUT_MIN < T_OUTPUT (current cycle) < T_OUTPUT_MAX
On the CORE processing Unit

## Slide 10
CYCLE i-1
CYCLE i
CYCLE i+1
Application
Application
Application
Constants : T_CYCLE_MIN, T_CYCLE_MAX, T_APPLICATION_MIN, T_APPLICATION_MAX
  T_CYCLE_MIN < T_CYCLE (current cycle) < T_CYCLE_MAX
  T_APPLICATION_MIN < T_APPLICATION (current cycle) < T_APPLICATION_MAX
On the CORE processing Unit; more abstract view
Those constants / performance / SW design (buffering, …) are related.
Safety : it is assumed there is a watchdog macanism

## Slide 11
CYCLE i-1
CYCLE i
CYCLE i+1
Input
Application
Ouput
Input
Application
Ouput
Input
Application
Ouput
Input_I1 at
ETCS external
interface
Output_O1 at
ETCS external
interface
Input_I1 acquisition
Output_O1 processing
application
treatment
Peripherals + CORE processing Unit (1/2)

## Slide 12
CYCLE i-1
CYCLE i
CYCLE i+1
Input
Application
Ouput
Input
Application
Ouput
Input
Application
Ouput
Input_I1 at
ETCS external
interface
Output_O1 at
ETCS external
interface
Input_I1 acquisition
Output_O1 processing
application
treatment
Peripherals + CORE processing Unit (2/2)
(« input treatment at next cycle »)

## Slide 13
Peripherals + CORE processing Unit; more abstract view
CYCLE i-1
CYCLE i
CYCLE i+1
Application
Application
Application
Constants : T_CYCLE_MIN, T_CYCLE_MAX, T_APPLICATION_MIN, T_APPLICATION_MAX;
For each INPUT (I1, I2, ….) : T_INPUT_ACQUISITION_MIN, T_INPUT_ACQUISITION_MAX
  For each OUTPUT (O1, O2, …) : T_OUTPUT_PROCESSING_MIN, T_OUTPUT_PROCESSING_MAX
T_CYCLE_MIN < T_CYCLE < T_CYCLE_MAX
T_APPLICATION_MIN < T_APPLICATION < T_APPLICATION_MAX
For each INPUT (I1, I2, ….) : T_INPUT_ACQUISITION_MIN < T_INPUT_ACQUISITION < T_INPUT_ACQUISITION_MAX
For each OUTPUT (O1, O2, …) : T_OUTPUT_PROCESSING_MIN< T_OUTPUT_PROCESSING < T_OUTPUT_PROCESSING_MAX
Input_I1 at
ETCS external
interface
application
treatment
Input acquisition (T_INPUT_I1_ACQUISITION_MIN)
Input acquisition (T_INPUT_I1_ACQUISITION_MAX)
Output_O1 at
ETCS external
interface
Output_O1 at
ETCS external
interface
(in case of application treatment at cycle i)
Can be more than 1 cycle !!!
Cycle independant.
Output processing (T_OUTPUT_O1_PROCESSING_MIN)
Can be more than 1 cycle !!!
Cycle independant.
Output processing (T_OUTPUT_O1_PROCESSING_MAX)

## Slide 14
Peripherals + CORE processing Unit; other view
CYCLE i-1
CYCLE i
CYCLE i+1
Application
Application
Application
Constants : T_CYCLE_MIN, T_CYCLE_MAX, T_APPLICATION_MIN, T_APPLICATION_MAX;
For each INPUT (I1, I2, ….) : T_INPUT_ACQUISITION_MIN, T_INPUT_ACQUISITION_MAX
  For each OUTPUT (O1, O2, …) : T_OUTPUT_PROCESSING_MIN, T_OUTPUT_PROCESSING_MAX
T_CYCLE_MIN < T_CYCLE < T_CYCLE_MAX
T_APPLICATION_MIN < T_APPLICATION < T_APPLICATION_MAX
For each INPUT (I1, I2, ….) : T_INPUT_ACQUISITION_MIN < T_INPUT_ACQUISITION < T_INPUT_ACQUISITION_MAX
For each OUTPUT (O1, O2, …) : T_OUTPUT_PROCESSING_MIN< T_OUTPUT_PROCESSING < T_OUTPUT_PROCESSING_MAX
Input_I1 at
ETCS external
interface
application
treatment
Input acquisition (T_INPUT_I1_ACQUISITION_MIN)
Input acquisition (T_INPUT_I1_ACQUISITION_MAX)
Output_O1 at
ETCS external
interface
Output_O1 at
ETCS external
interface
(in case of application treatment at cycle i)
Can be more than 1 cycle !!!
Cycle independant.
Output processing (T_OUTPUT_O1_PROCESSING_MIN)
Can be more than 1 cycle !!!
Cycle independant.
Output processing (T_OUTPUT_O1_PROCESSING_MAX)
Input_I1 at
ETCS external
interface

## Slide 15
Providing TIME to the Application

## Slide 16
Time, MMU & Balise : Putting all together
Balise telegram
Balise Center Timestamp (Time when the train antenna passed the center of the balise)
Balise Center Odo_stamp (position) minimum, maximum, nominal
Max error on Balise center position detection (constant = 1m)
T_Balise_input_acquisition_min (constant)
T_Balise_input_acquisition_max (constant)
ETCS time data for application
T_Time_input_acquisition_min (constant)
T_Time_input_acquisition_max (constant)
MMU data (distance, speeed, ..) min, nom, max
MMU data Timestamp (time related to the MMU data computation)
T_MMU_input_acquisition_min (constant)
T_MMU_input_acquisition_max (constant)
All Time values are taken in the same referential => can be compared together
All distance values are taken in the same referential => can be compared together
T_CYCLE_MIN, T_CYCLE_MAX (constant)
T_APPLICATION_MIN, T_APPLICATION_MAX (constant)
Open ETCS
Application
Open ETCS
Application
OUTPUTS